## Slide 1: Networked systems & protocols
Part 1
Computers need Telecommunications
Notes: In this introductory chapter, through the historical evolution of telecommunications, Some main concepts will be introduced. Explaining concepts as they were initially implemented is interesting because at that stage they were still reduced to the essentials and not cluttered with lots of irrelevant “improvements” mainly motivated by marketing considerations.

## Slide 2: Remote Access to Computers (1970)
Star Network
Mainframe Computer
Dumb Terminals
Notes: The electronics revolution resulting from the generalized use of semi-conductor devices did not only have an influence on consumer electronics but also on corporate computers. These machines became very powerful and their capacity extended often well beyond the needs of a single user. Such powerful computers became also the kernel of centralized data repositories in large organizations.
All this implied giving remote access to users. Dumb terminals (basically a screen and a keyboard) were connected to central computers by means of a star-like access network.

## Slide 3: Integrated Services Digital Network The first attempt to integrate voice and data
Voice digitized at 64 Kb/s (8000 samples/s, 8 bit)
Truly digital signaling
A telephone connection = a 64 Kb/s digital link
A 64 Kb/s digital link is excellent for connecting a dumb terminal to a mainframe computer
Connection time billing inadequate for data
ISDN widely used for telephony
ISDN marginal for data applications
Notes: Connecting remote terminals to central computers was a new and challenging business for telecommunications operators:
If the analog telephone network was to be used, digital data needed to be encoded as analog signals with properties similar to those of the human voice. This could be done by means of MODEMS (MODulators-DEModulators) but throughput could never exceed 33 Kb/s due to the limited bandwidth offered by the analog switched telephone network and transmission was quite sensitive to noise on the telephone lines.
In the late sixties, telecommunications operators designed a new network, called ISDN (Integrated Services Digital Network) intended to support data communications (mainly between dumb terminals and central computers) and digitized voice traffic.
This technology was widely adopted at the level of the trunk lines and the switches, but got little success in the local loops and the end-users terminals.
The lack of success with end-users could be explained by observing that ISDN didn’t bring significant new services to the telephone user and appeared as too slow and too expensive for connecting terminals with central computers. ISDN was too expensive for most data applications because its billing was based on connection time rather than on data volumes while data traffic tends to be very bursty, with a low average throughput but with very long connection times.

## Slide 4: Local Area Networks (1970)
LAN’s initially introduced for
  Printer sharing
  File sharing
  ...
Notes: The introduction in the seventies of personal computers led to the development of local communications networks allowing these personal workstations to share, at that time still very expensive and voluminous, peripheral devices such as printers and disks. These local area networks, designed within the computer industry used totally different technologies than those popular in the wide area networks operated by the telecommunications industry. The local area networks featured data rates in the range of Mb/s over distances of a few hundred meters.

## Slide 5: The Dual Screen Desk (1980)
WAN
LAN
LAN
Notes: The success of personal computers and local area networks in office automation and the generalization in business of large centralized databases with remote access through dumb terminals led to an awkward work environment were many employees needed a personal computer and a dumb terminal to perform their work. Transferring data from one environment to the other implied most often retyping.

## Slide 6: LAN-WAN Integration (1990)
WAN
LAN
LAN
LAN
Notes: Lots of efforts were done in the eighties to make wide area and local area networks compatible. Communication techniques suitable for both were developed.
These efforts resulted in a complete change of the role of long distance networks: instead of connecting terminals to computers they were used to interconnect local area networks.

## Slide 7: Client - Server Systems
Interconnection Network (LANs+WAN)
Notes: The possibility of interconnecting easily computers resulted in a new architecture for data processing systems called “client-server” systems.
End-users got personal computers, called “clients”, optimized for user-friendliness, but often limited in storage capacity and processing power.
These clients could access through the network the resources of specialized servers, providing shared storage, shared peripherals and shared processing power.

## Slide 8: 70’s: Need for Open Networks
CCITT/ISO start standardization work for
Open Systems Interconnection
ARPA finances Research on open Network Technology:
  a Research WAN, ARPANET
  research on LAN interconnections
Combination of the two ARPA efforts resulted in the INTERNET
Notes: In the seventies, the necessity to develop communication technologies making local and wide area networks compatible became obvious.
The telecommunications industry, through the “Comité Consultatif International pour la Téléphonie et la Télégraphie”, a body of the United Nations, undertook to define a set of standards that would ensure seamless interoperability of conformant networks and equipment. In line with the traditions of the telecommunications industry, connection oriented approaches to networking were preferred because they allowed strong quality of service (QOS) guarantees.
In the United States, several research departments, with close ties with the computer industry, got financial support from the “Advanced Research Projects Agency” to interconnect their local area networks via long distance links. This project was quite successful and resulted in what is now called “the Internet”. In line with the existing experience with local area networks, a best effort without any guarantees approach was preferred because it maximized resource sharing and minimized the management overhead. Moreover QOS was not considered important for data transfers between computers.

## Slide 9: The Early ARPANET (1976)
Hawaii
London
Satellite link
56 Kbps terrestrial link
Vince Cerf
Notes: The early network that was implemented interconnected a dozen of research centers spread over the USA plus one located in London. The links were 56 Kb/s lines leased from the telephone company, with the exception of the links connecting University College in London and the University of Hawaii that were satellite links. This network was called “Arpanet”.
Hundreds of researchers cooperated on the design and the implementation of this network. Among them Vince Cerf played an important role and is often called “father of the Internet”. Presently Vince Cerf directs research at Google.

## Slide 10: The Results:
TCP/IP + Set of Application Protocols
  Set of communication “standards” allowing interoperability of almost all brands of computers.
  Applicable to
    Local Area Networks
    Wide Area Networks
    Interconnection of LAN’s through WAN’s
The INTERNET
  Communication facility for the Research Community
  Financed by US government
Notes: Apart from Arpanet, that allowed participating researchers to communicate efficiently with each other and served as a test bed for communications software and applications, the research produced a set of communication protocols and remote applications that could be used as well on local as on wide area networks.
The communications protocols developed for Arpanet are often collectively called by the combined name of two of them “TCP/IP”.

## Slide 11: The success story of TCP/IP
To connect a computer to the ARPANET, TCP/IP is required !
Many different computers in use in Universities and research centers.
TCP/IP becomes THE networking software available on ALL machines.
Many stand-alone networks using TCP/IP appear due to the wide availability of TCP/IP and the many applications available for it.
Notes: Protocols and software developed for Arpanet was freely available because they had been financed by government grants. As the different groups involved in Arpanet used a wide variety of different computers the project became de facto a source of free good quality communications software available on almost all computers, regardless of their vendor.
As a consequence all over the world TCP/IP became the best choice for interconnecting computers, even when totally unrelated to Arpanet.

## Slide 12: The success story of ARPANET
      Universities where TCP/IP was developed start using the ARPANET backbone as a general purpose communication network.
Other universities and research centers also want to get connected: with the help of the NSF, ARPANET becomes the North American Research Network.
FREE access but “Acceptable Use Policy” imposed by ARPA on all users.
Exponential growth of number of users
Enormous help for US researchers.
Notes: Once operational, Arpanet started to be used not only for research on networking but also as a powerful and versatile communications medium available for free to the connected research centers. Soon neighboring departments started also to use the network and quickly Arpanet became a general purpose communications network for the entire north American research community.
Once fully operational, Arpanet could hardly be considered as an advanced research project and ARPA no longer financed the running of the network that changed its name into Internet..
Part of the cost of Internet was taken care of by the US National Science Foundation but new sources of financing were clearly needed.

## Slide 13: The first internet virus November 2, 1988
      .
Designed by Robert T. Morris from Cornell University
Intended to measure the size of the Internet
Got out of control and invaded some 6000 machines
Digital VAX and SUN machines running UNIX were invaded.
Invaded machines contaminated other machines and, recursively, themselves, finally blocking them.
The entire Internet was out of order for several days
R.T.Morris was sentenced 400 hours community services and a fine of $10 050
He is now a tenured professor at MIT.
Notes: The first widely noticed harmful program invading the Internet was an email that, using some bugs in UNIX 4BSD (no testing on the size of arrays),
Accessed the local mailing lists and did send itself to all addresses in those mailing lists. When arriving in a machine, it checked if it was already present in that machine. If so it would not operate on that machine, but, to avoid a too simple way to stop the propagation by installing an harmless program mimicking the invader, a provision was made to ignore the presence of the invader in 1 out of 7 cases. This resulted in recursive infection of machines by themselves until they were blocked by lack of memory space.

## Slide 14: Major Internet Changes 1989-1992
DARPA is no longer the major funds provider.
Apparition of the .COM domain
Backbone operated by private companies and paid by the US-NSF and the connected networks.
“Acceptable Use Policy” no longer required on the backbone, even if many of the connected networks still have one.
Commercial “Internet Service Providers” build private networks to connect their subscribers to the Internet.
The Internet has become a set of independently financed, cooperating regional networks.
Notes: Allowing private companies to use the Internet, first for research related communications and later also for commercial and marketing purposes, provided the needed alternative funding.
Commercially operated companies, called “Internet Service Providers”, started to build networks to give private users access to the Internet.

## Slide 15: Internet Cost Structure
GéANT
- Backbone infrastructure and neutral interconnects
paid by interconnected networks, proportional to
their access bandwidth.
- Cost of direct interconnects shared by partners.
.
USA
Renater
Orange
fr
Belnet
VOO
Skynet
Telenet
Mobistar
be
Notes: Nowadays the Internet is a set of independent, mostly privately owned networks interconnected by means of “Neutral interconnection Points” or jointly financed backbone networks, often operated by commercial enterprises.
A neutral interconnection point is the interconnection of different networks in a single point and a backbone network is a high throughput network carrying messages from one network to an other.

## Slide 16: Network Choice
Dublin:
24 Networks
London:
30 Networks
Madrid:
40 Networks
Zurich:
30 Networks
Vienna:
91 Networks
Stockholm:
21 Networks
Copenhagen:
21 Networks
Dusseldorf:
40 Networks
Frankfurt:
156 Networks
Amsterdam:
38 Networks
Paris:
53 Networks
Brussels:
34 Networks
Over 350 Carriers/ISPs
The broadest range of
network providers of any data centre operator in Europe
Notes: This slide and the following, kindly provided by a company that sells computing services, gives an idea of the multitude of Internet Service Providers and Neutral Interconnection Points active in western Europe in 2010.

## Slide 17: Exchange Choice
SFINX
ParIX
18 Leading Internet Exchanges
4 Carrier Ethernet Exchanges
The broadest range of Exchanges with the largest aggregated traffic volume of any data centre operator in Europe

## Slide 18: The Multi-media challenge
Voice & Images
Data
Correctness:
Non-essential
Essential
Delay:
Small & Stable
Unimportant
The notion of “Quality of Service”
Conclusion:
Data and multi-media traffic have
totally different requirements
Mixing them on a single network is
technically and economically challenging
Notes: Using a single network both for data and multimedia traffic is quite challenging, because the requirements for these two types of traffic are quite different:
For data traffic, correctness is essential, while delay is of lesser importance.
For multi-media traffic, a small number of transmission errors is acceptable but long and, even worse, variable delays are quite unacceptable because they disrupt the flow of sound or images.

## Slide 19: The Cloud The ultimate client-server.
The Internet ensures universal connectivity.
This connectivity can be restricted by the network management (= “Software Defined Networks”)
The “Cloud” = set of resources owned by operators
  processing power,
  specific application software
  storage,
  …
Cloud available to clients via service agreements.
Location and ownership of resources not visible
Notes: The Internet provides connectivity between all connected devices, often with very high throughput.
Building, hardware wise, complex system architectures, such as those for client server systems is no longer required, as it is possible to define, by the network management software, which data flows are allowed and which are not (= “Software Defined Networks”)
A modern view of the Internet consists in considering a set of resources such as processing power, specific application software and storage, owned by private operators, and made available to specific clients via service agreements.
As neither the owner nor the location of the resources is clearly visible, those are said to be located in “the cloud”.

## Slide 20: The Internet of Things Stand-alone Sensor and Actuator Networks
Low cost intelligent sensors and actuators
For
  Industrial process control
  Drivers assistance in cars: GPS, slippery roads, etc.
  Domotics: temperature control, lights, etc.
  Security: movement, broken windows, doors, sirens, etc.
  Personal health management: sports monitoring
Wires costly and inconvenient: Wireless, battery powered
Remote control and reporting desired
  Via telephone or GSM
  Via the Internet
Notes: The progress in electronics resulted in the nineties in in a broad choice of good quality, low cost, sensors capable of measuring localization, temperature, humidity, light, movement, acceleration, heart pulse, etc. Low cost microprocessors became available to analyze the collected data and many devices, controlled by the microprocessor could provide feedback to the observed processes. This resulted in an exponential growth of the so called “intelligent” systems in cars, in homes and even in leisure activities. Simple interactions with the users remained however problematic, as the processing power and the displays for user-friendly graphical interfaces were not available.

## Slide 21: A wireless thermostat
Remote control via Internet: available and OK
Interfacing with physical systems: a nightmare
Too many proprietary systems !!!
Notes: Many automation, monitoring and entertainment systems exist. Many have internet interfaces, but connecting them to existing equipment such as locks, central heating systems, lighting, water distribution systems, etc is very expensive and even impossible when these systems have different brands because each manufacturer uses proprietary protocols, mainly because they want to sell services rather than equipment.