## Slide 1: Networked systems & protocols
Modeling Communication Systems

## Slide 2: Layered Network Models
The problem:
  Complexity of networked systems
The solution:
  Decomposition into independent subsystems
Layered network model
  Introduced by IBM (SNA, 1971)
  Standardized by ITU (X200) and ISO (7498)
  Method universally adopted
  Standards not really obeyed in practice
Notes: Telecommunications systems can be extremely complex. In order to keep that complexity under control it is necessary to subdivide the systems into a certain number of subsystems, which are as independent from each other as possible.
Starting with SNA, announced by IBM in the early seventies, computer networks have systematically been designed as a set of independent functional layers.
The"Comité Consultatif pour la Télégraphie et la Téléphonie", now renamed "International Telecommunications Union" and the "International Standardization Organization" have, in the late seventies, tried to develop a formal framework for layered systems, called the “Seven layers OSI (Open Systems Interconnection) model" (ITU recommendation X200, ISO standard 7498.
The concepts and the broad lines of the seven layers framework they proposed are universally used to describe networks, but the actual protocols that were developed in that context are by now abandoned in favor of the Internet protocols, developed independently from these standardization bodies.

## Slide 3: A diplomatic negotiation
Translation
Cryptography
Transmission
Service Access Points
Political arguments
Notes: To understand the ideas underlying a layered model, the technical issues associated with an imaginary international negotiation will be approached in the same way as network issues are.
Two presidents, X and Y, physically present in different towns Tx and Ty, speaking exclusively different languages Lx and Ly, want to discuss some important issue.
Hopefully, they both know enough about each other’s susceptibilities to be able to have a meaningful negotiation. This can be summarized here by stating that they have (implicitly) agreed upon some “diplomatic rules” which they obey to exchange political arguments.
In order to negotiate, they, however, need some support services which would allow them to overcome the difficulties resulting from the language differences and from the distance. In addition they want that these services should be provided in such a way that the contents of the negotiation are kept secret. In other words, they should need some kind of secure telephone service, providing also translation. In the slide this service is depicted as a black box, labeled "Communication Services", accessible by X and Y through "Service Access Points".
The communications services design translation, cryptographic and transmission services.

## Slide 4: A diplomatic negotiation
Cryptography
Transmission
Service Access Points
Political arguments
Single language messages
Notes: If the inside of the black box would have a layered structure, one would find, directly underneath the service access points, two entities providing a specific service, and using for that the services provided by an inner black box.
The outer entities in this example would be translators showed in the slide. Each president would have, next to him, a translator. These translators should obviously be fluent in the language spoken by their president. In addition, they should also be fluent in some common language Lc, to be used for communicating with each other. Lc could be one of the languages Lx or Ly, but this is in no way required, and in fact, as long as the presidents trust the quality of the service provided by their translators, nobody but the translators themselves should worry about Lc.
One should notice that how the services are obtained through the service access points doesn’t need to be identical on both sides. For instances one could imagine that president X is on very friendly terms with his translator and conveys a lot of information just trough body signs while president Y communicates very formally, by phone with his translator.
The translators communicate with each other by means of the services provided by another black box.

## Slide 5: A diplomatic negotiation
Political arguments
Transmission
Service Access Points
Single language messages
Encrypted messages
Notes: This slide shows the inside of the previous black box providing cryptographic encoding that fulfills the confidentiality requirement. Encryption and decryption is done by means of some cryptographic key Kc, which should be kept secret. Only the operators of the cryptographic devices in Tx and Ty should have access to the key.
The cryptographic devices communicate by means of the services provided by still another black box.

## Slide 6: A diplomatic negotiation
Political arguments
Service Access Points
Encrypted messages
Single language messages
Electromagnetic waves
Notes: Inside the last black box, radio equipment ensuring the actual communication between Tx and Ty is to be found. The operators of these two radio sets should obviously agree about tuning to some common frequency Fc, about using some common modulation scheme, etc. It is again clear that the choice of the physical parameters of the communication is of no concern to the users of the service, who, most probably, do not even know what frequency modulation or a megahertz might be.

## Slide 7: Layered Model Definitions
Level (n+1)
entity
Level (n+1)
entity
Level (n)
entity
Level (n)
entity
Level (n-1) Service Provider
Level n
Service Access Points
Level n Addresses
Virtual level n+1 communication path
using a level n+1 protocol
Virtual level n communication path
using a level n protocol
Physical Communication Path
Notes: In the previous example, a complex communication problem has been decomposed in 4 independent layers following some general principles schematically represented in this slide.
Each layer solves one specific problem. Layer n offers services to level n+1 through level n service access points. From the point of view of layer n, the different entities of layer n+1 are identified by their level n address.
Entities at level n communicate with each other according to some rules agreed specifically for that layer (the language Lc, the cryptographic key Kc and the frequency Fc). Such "horizontal" agreements are called "protocols of level n".

## Slide 8: Layered Model Definitions Example: The Telephone Service
Telephone Network
Telephone
Service Access Points
Telephone Numbers
Virtual Interpersonal communication path
Physical Communication Path
Notes: The traditional telephone network can be used as an example to clarify the introduced notions: The telephone service carries sound between two service access points which are telephone sets. The telephone network has more than two service access points (over 109 actually) and all these access points are identified by means of their address, the telephone number.

## Slide 9: Layered Model Definitions Protocol Data Units
Level (n+1)
entity
Level (n+1)
entity
Level (n)
entity
Level (n)
entity
Level (n-1) Service Provider
(n+1)PDU
(n)PDU
Notes: It is important to observe that entities of level n communicate with each other without a direct communication channel between them. They communicate via a virtual channel, which is implemented by the underlying layers. A message send from one level n entity to an other (called "level n Protocol Data Unit", or nPDU in the OSI jargon) will in fact be entrusted to layer n-1, which will encapsulate it in a (n-1)PDU, which will, in turn be entrusted to layer n-2, etc. The message which is finally transmitted physically is likely to be much longer than the one generated at level n, as all of the intermediate layers add their own service information to it.
To further clarify the involved mechanisms, one could consider in this slide the two entities of level n+1 as two people A and B, A wanting to send a letter to B by courier service.
The courier service is accessed through the level n entities: an employee puts the letter from A in a specific envelope with all the service information the courier service needs to properly deliver the letter at B.
This letter, in its envelope, is then transported to office of the couriers service in B’s town, This transportation is done by a level (n-1) service provider.
In B’s towns, another employee of the courier service brings the envolope to B’s office, removes the letter from the envelope, discards the envelope and gives the letter to B.

## Slide 10: Layered Model Definitions Layer overhead
Level (n+1)
entity
Level (n+1)
entity
Level (n)
entity
Level (n)
entity
Level (n-1) Service Provider
Connection oriented protocol
Notes: It is even possible as shown in this slide that one (n+1)PDU results in several nPDU's.
For example, this is the case when the level n protocol requires a connection to be established before any data can be transferred and that the opening and closure of a connection do require the exchange of many messages..

## Slide 11: Connection oriented communication
Typical example:
A telephone conversation
3 step process:
1. Establish connection
  using the signaling protocol
2. Use connection
  using an informal protocol
  being billed for duration of usage
3. Terminate connection
  using the signaling protocol
Notes: Communication by telephone can be decomposed in three clearly distinct phases: first, by means of a certain signaling protocol, the user requests the telephone company to connect his or her set with another one identified by a number (an address). When this has successfully been done, a bi-directional communication channel is available between the two telephone sets and the conversation can take place. The Telephone Company monitors this channel for billing purposes and to close it when requested to do so by the initiator of the call.

## Slide 12: Connection oriented communication
A temporary communication channel
is build through the telephone network
Notes: In a connection oriented protocol, a virtual link between two addresses is established, used and deleted.
- 1. Upon request of a user, the network management establishes a connection between two addresses a and b. In its request the user has to specify the addresses a and b as well as the characteristics of the requested connection. The network management chooses a route in function of the available resources, or, refuses the request if no sufficient resources are available.
- 2. Once the connection has been established, the user can transfer data between a and b, without having to mention any more these addresses. Normally network management continuously monitors all connections to bill their utilization and to detect and correct possible malfunctions.
- 3. Finally, the user requests closure of the connection.
Before data transmission can start a lot of work has to be done, but once the connection established, data transfer is extremely simple and efficient.

## Slide 13: Connection oriented communication Main points
Network has a state : the list of active connections
Network can guarantee Quality Of Service
  Reservation of transmission capacity at connection establishment
  Monitoring of data transfer and correction of transmission errors by retransmission
Network is fragile : state can be lost.
Application domain :
  Very efficient for transferring high volumes of data
  Mandatory if stringent Quality Of Service requirements
  Poor initial response times due to connection setup
  Inapplicable if nodes have high failure rate.

## Slide 14: Connectionless communication
Typical example:
The postal service
Letters, with an address and a stamp,
are individually carried from a
Post office box to a personal mailbox
Notes: In postal services no preliminary setup is needed to send an ordinary letter from point A to point B. It suffices to drop the letter, with its destination address and proof of payment for the service, in a letter box at A. The post office will collect the letters in the letter boxes, sort them according to destination, transport them to their destination and drop them in the desired mailboxes.
No connection whatsoever is established, no records about individual letters is kept.
As the number of letters dropped in the different letter boxes can vary widely, no guarantees can be given about how long it will take to sort and deliver all letters.

## Slide 15: Connectionless communication
No connections are needed to carry mail
Notes: These services are extremely simple: users transmit packets of data to a service provider who tries to deliver these packets as soon as possible at the address included in the packet. No initial delay for connection establishment is needed but routing has to be decided independently for each packet, even if they all have the same destination, and, as reservation of resources can only be done on a statistical basis, severe delays and even packet loss can be caused by congestion problems.
As each data packet is handled separately no connection list is to be maintained and no record of transmitted packets is normally kept. The network is stateless.
Connectionless communications seem to be adequate when small volumes of data have to be send to various destinations and when short response times are important.

## Slide 16: Connectionless communication Main points
The network is stateless.
No guaranteed Quality Of Service.
  No reservation of transmission capacity
  No error correction by retransmission
Network is robust :
  No state stored in any node
  Each node operates almost independently from others
Application domain :
  Whenever single message response times are critical
  Whenever nodes are unreliable

## Slide 17: A two layers model.
Applications Layer
Networks Layer
Connectivity
Interoperability
# Interfaces = # Applications * # Networks
Notes: A first model, based on just two layers, establishes a distinction between “connectivity and interoperability. The example of the "plain old telephone service" shows clearly the difference: thanks to a world-wide numbering scheme and the interconnection of all the national telephone networks, it is fairly easy to establish a telephone connection between two arbitrary points in the world to carry sounds between these two points. This is worldwide connectivity. If, however, people want to interoperate (do meaningful things) through the telephone, they should not only be able to exchange sounds, but also to understand each others sounds, i.e. to listen when the other speaks and vice versa, to use a common language and to talk about subjects they are both knowledgeable about.
In this model, the lower layer, called “networks layer” provides the connectivity service while the upper layer, called “application layer” handles the additional issues to make the connectivity useful.
Even in a single connectivity network, it is likely that different communication technologies need to be used as distances can vary widely and as some users have fixed locations while others are mobile. Different network entities must coexist.
As a single network service can be used for a broad range of applications, several different application entities will need to be interfaced with the different network entities. In fact, if n different network entities exist and m different application entities, n*m interfaces will need to be made available.

## Slide 18: A three layers model.
Applications Layer
Internet & Transport Layer
Networks Layer
Connectivity
Interoperability
# Interfaces = # Applications + # Networks
Notes: In order to reduce the number of interfaces between network entities and application entities, generally one additional layer, called “Internet and Transport layer” is inserted between the networks and applications layers.
This way, only n+m instead of n*m interfaces are needed.
Moreover, the intermediate layer can be used to enhance the services offered by some networks to the service level required by some applications.
For instance, some applications require a connection oriented connectivity service, while the available networks only offer connectionless services. In such circumstances, the intermediate layer can add connections to the underlying services.

## Slide 19: The Internet & Transport Layer
Applications Layer
Internet Layer
Transport Layer
Networks Layer
Notes: As in the internet, the role of the lower layers, those that ensure connectivity between devices, called “hosts” can be implemented by a broad variety of technologies, the lower part of the intermediate layer, called “internet layer” requires the simplest possible service from them. This is a connectionless, unreliable service that carries individual data packets from one host to another. The Internet layer is responsible for identifying all connected hosts by a unique address, the IP address of the host. Some hosts, called “routers” are connected to several networks. They have a different IP address in each network and are used to transfer packets from one network to another. Router software has no layers above the internet layer.
As in a host several different programs can need to communicate via the internet, the upper part of the intermediate layer, called “transport layer” distinguishes these programs by assigning them a specific address, called “port number”. Some transport protocols just handle port numbers, others, in addition to the port numbers, handle the establishment, the use and the closure of transport layer connections.

## Slide 20: The Internet & Transport Layers Example: www
TCP
Networks Layer
http
SKYNET
UUNET
IP
IP
Notes: As an example, one could consider the world wide web.
At the application level one finds the http protocol and browsers such as Chrome or FireFox that are application entities on the client side and web server software such as Apache on the server side.
The intermediate layer implements the TCP and IP protocols. The underlying networks are those provided by various Internet Service Providers (ISPs), such as, In Belgium, Skynet or Uunet or Belnet.
At the interconnection points between the networks of these ISPs, one finds IP entities but no TCP entities, as the transport entities are only to be found together with the application entities.

## Slide 21: The 7 OSI layers
Applications Layers
Internet & Transport Layer
Networks Layers
Connectivity
Interoperability
1 : Physical
2 : Data Link
3 : Network
4 : Transport
5 : Session
6 : Presentation
7 : Application
Notes: The “Open System Interconnection” model uses 7 layers rather than 3.
The applications layer of the 3 layers model is subdivided into three layers: The upper layer provides the “Application Programmers Interface” (API) between the networking software and the specific applications.
Underneath, the presentation layer (6) handles issues about data syntax and semantics while the session layer controls application synchronization (one application should listen when the other is sending).
The transport sublayer of the three layers model is on its own layer 4 of the OSI model.
All addressing and routing issues handled by the Internet and Network layers of the three layers model have been grouped into a single third OSI layer called “Network layer”.
Underneath, the “Data link layer” packages data in frames compatible with the physical transmission means and controls the transmission of these frames, performs transmission error detection and, if desired, error correction through retransmission of erroneous frames.
The bottom layer, called “Physical layer” cares for the physical details of actual data transmission, such as encoding bits by means of electrical waveforms.

## Slide 22: Hierarchical Addresses
Addresses composed of meaningful fields
Address = hierarchical list of domain names
A domain is an organizational and/or geographic entity regrouping lower level domains or hosts.
Addresses belonging to a given domain are maintained by the authority of that domain.
Example : classical telephone numbers
  32 2 629 2905, 32 47 5819327
  hierarchy jeopardized by number portability!
Notes: When assigning addresses, two different approaches are possible:
The address contains some information about the owner or it contains none.
When addresses contain some information, the address can be subdivided in different hierarchical fields, each field conveying some information about the localization or the owner of the address. Such addresses are called “hierarchical addresses”.
For instance, classical telephone numbers contain a lot of information about the their localization: from the telephone number 32 2 629 2905 one can derive by looking at the two first digits (32) that the number is in Belgium and by looking at the next digit (2), that it is in Brussels, The next three digits (629) identify the Proximus exchange (Borrensstreet in Elsene) and the next digit (1, 2 or 3) the private exchange of the VUB. The last three digits identify a specific line connected to the private exchange of the VUB.
With such a hierarchical numbering system, each country can maintain a database with its users, and the first digits of the number indicate which data base contains the relevant information.
Remark. The telephone numbers in Belgium have lost part of their hierarchical character as a telephone user can keep an original number when switching between telephone providers. If the VUB were no longer a Proximus customer it would no longer physically be connected to the exchange in the Borrensstreet. It would have an other (invisible) number belonging to an other operator. When the VUB would be called, a database of ported numbers would be consulted to find the number the VUB would have with its new provider.

## Slide 23: Flat Addresses
Organizational and geographic hierarchy do not necessarily match
Address values contain no useful information
Example : Internet network ID’s
  VUB = 134.184 ULB = 164.15
  KUL = 134.58 KULAK = 193.190
  RUG = 157.193
Using large set of flat addresses user-unfriendly
Solution :
Assign a flat and an hierarchical address to every user and maintain a database linking both
Notes: As was already shown in the previous slide, maintaining hierarchical addresses consistently becomes more and more difficult as organizational schemes no longer have to match physical implementations.
For that reason, it is often decided that physical addresses should not convey any contextual information (except maybe the date of assignment as most addresses are then assigned in sequential order),
Such flat addressing scheme puts however a heavy burden on the directory database, as a single database should contain all addresses.
This problem can been solved by assigning physical flat addresses and logical hierarchical addresses to users. Based upon the hierarchical logic addresses, the directory can be decomposed in a hierarchy of locally maintained databases that map logical and physical addresses.
The Domain Name System (DNS) implements such a distributed directory for Internet users.

## Slide 24: Internet Domains
uk
Root
ibm
vrt
be
ac
ulb
tiberghien
vub
mtv
ieee
com
org
edu
tiberghien@vub.ac.be
etrovub
tiberghien
tiberghien@etrovub.be
Notes: Next to its physical internet address, (which is presently a 32 bit binary number, that is progressively being replaced by a 128 bit number) each host on the Internet has a logical address that fits into a hierarchy of domains. Each domain can contain other domains and local hosts. In each domain a local database, called “Domain Name Server” (DNS) keeps the list of subdomains and the list of the local hosts, together with the corresponding physical addresses (the physical address of a subdomain is the address of the DNS server of that subdomain).

## Slide 25: Some Applications: Domain Name Servers
In Each domain, there is at least one DNS
  Name & DNS Address of all subdomains
  Name & address of all hosts in the domain
  DNS address of, at least, root of DNS system
  Names & DNS addresses of frequently used domains
Each host must know the address of one DNS
Address resolution can be done recursively or by successive calls to different DNS
Local DNS is locally maintained
Caching greatly improves performance of DNS by keeping the translations of most recently accessed domains and hosts

## Slide 26: Some Applications: Domain Name Servers
a@m1
d@m4
c@m4
b@m2
m4
d@m4
INTERNET
m4 is a “mail server”, with a mailbox for each registered user.
Connection between mail server and users can be temporary
(direct or via internet)
Notes: Basically, email is a technique that allows somebody to save a file on somebody’s else computer.
As one can hardly expect that the computers of people one wants to send mail to are always on and reachable, mail servers have been introduced: these machines are always on and reachable and have specific storage space, called mailboxes, to store incoming mail for their clients. The actual users can then access their mailboxes whenever is convenient.
In the X400 standard developed in the context of OSI for electronic mail systems, the mail server managing the mailboxes was called the “Mail Transfer Agent” while the computer used to actually send and receive mail were called “User Agents”. While the X400 standard is no longer popular, the MTA and UA acronyms continue to be used.

## Slide 27: Email Protocols
Eudora
Outlook
Exchange
Netscape
a@m1
d@m4
c@m4
b@m2
m4
SMTP
pop3
imap
(X400)
http
Pop/imap server
Mail Transfer Agent
(X400)
User
Agent
Notes: Two different application level protocols are needed for email: the first is used to transfer mail from the sender UA to the destination mailbox on the MTA. The most commonly used protocol for that purpose is the “Simple Mail Transfer Protocol” (SMTP).
The second protocol is used for communication between a mail server and its clients. Two specific protocols are widely used for that purpose, the Post Office Protocol (POP3) and the Interactive Mail Access Protocol (IMAP). The main difference between the two is that normally POP downloads the contents of the mailbox of the clients while IMAP leaves the mails in the mailbox but allows the user to read and manage them
More and more mail servers support not only the POP and IMAP protocols but also the http protocol, allowing access to mailboxes through the web..

## Slide 28: Some Applications: Multi-media real-time communications
Cathy@vub.ac.be
The SIP server can handle both diversity in terminals and mobility of terminals
SIP
Notes: For managing mobility, which implies changing the addresses of devices without interrupting the flow of data to or from the mobile device, each mobile user needs to have a stable reference address, which runs, (for instance, other server software is available for that purpose) the Session Initiation Protocol (SIP). When a mobile user is active, he logs his mobile device (such as a smartphone) in his SIP server. The SIP server maintains a database of logged-in users, with their respective addresses and the properties of their device. When the address of the user changes due to mobility, the SIP server automatically, by means of a process similar to the mobile phone handover, updates its data base.
The popular internet phone system Skype uses SIP to manage conversations.

## Slide 29: SIP in Redirection mode
Home network
Visited network
Callers network
SIP
Redirection server
Mobility management
Session set-up
Actual
Data transfer
Most efficient data transfer
Caller has access to actual called address
Notes: When somebody wants to establish a voice connection with a SIP user, the connection is first established with the SIP server of that user, which informs the caller of the present address of the called. Whenever the called changes its address, the SIP server informs the caller of the new address to be used.

## Slide 30: SIP in Proxy mode
Home network
Visited network
Callers network
SIP
Proxy server
Mobility management
Session set-up
Actual
Data transfer
Longer transmission delays
SIP server can be bottleneck
Caller has no access to the actually called address
Notes: A SIP server using the redirection mode can seriously jeopardize the privacy of the called, as any caller can, via the address of the called, determine his/her physical localization.
For that reason, the SIP server often plays the role of a proxy for the called, forwarding itself the actual data transfer between caller and called.
Of course, such a SIP proxy server can become a bottleneck when many users share the same SIP server.

## Slide 31: Some Applications: World-wide web
Uniform, hypertext based, user friendly interface for distributed databases.
Inexpensive, high quality, browsers available for almost all computers.
Well over 109 pages available worldwide, mainly for public relations, publicity and electronic commerce.
As executable programs can be part of hypertext, web browsers are now a universal run-time environment for end-user applications
Notes: The world wide web is an application initially developed at the “Centre Européen de Recherche Nucléaire”(CERN) by Tim Berners Lee and Robert Caillau to enable physicists to consult with a uniform users interface a wide variety of databases, located anywhere on the Internet.
As the web became soon a powerful tool for marketing and information dissemination, the www application has become by far the most used application on the Internet.
Most firewalls block executable programs, to avoid virus invasions, but can not block web pages because everybody wants them. As hypertext can contain executable programs hidden in web pages, web browsers are by now the standard environment to execute programs loaded through the Internet, (“apps”) with, as a consequence, the need to include sophisticated security in every web browser.

## Slide 32: Technically, what is the Web ?
The WEB = Internet + HTML + URL + HTTP
HTML = Hypertext Mark-up language
  Multimedia document
    Normal text
    Graphics and images (stored in separate files)
    Sound (stored in separate files)
    Executable programs ( = applets in Java code)
  References to other hypertext documents = “Anchors”
    “clickable” normal text or image (icon)
    address (URL) where the corresponding document can be found
Notes: Basically, the web has three key ingredients:
The Hypertext Mark-up Language (HTML)
The Universal Resource Locators (URL)
The Hypertext Transfer Protocol (HTTP)
HTML is a powerful language for describing pages containing texts, pictures, sounds and even executable programs.
A URL is an address, anywhere on the Internet, where an HTML page is available.
A HTML page can also contain hyperlinks, that are, in fact, URL’s of specific pages. Pages referred to by an hyperlink are fetched when an icon associated with the hyperlink is clicked on. Some hyperlinks are not associated with icons and the corresponding pages are fetched whenever the page containing the hyperlinks is displayed. Such “automatic” hyperlinks are used, for instance, to add advertisements to web pages.

## Slide 33: Technically, what is the Web ?
The WEB = Internet + HTML + URL + HTTP
URL = Universal Resource Locator
Protocol used to communicate with resource
  (each protocol further defines URL format)
Internet Resource Address
  Domain name
    Internet Protocol address of machine (134.121.023.001)
    Domain Server Name of machine (www.vub.ac.be)
  Port number on machine
    Optional : Each protocol has a default port number
Resource details (protocol specific)
  (i.e. directory and filename of an HTML page)
http:
//www.vub.ac.be:80
/webpages/info.html
Notes: An URL is in fact an extended Internet address, Not only the address of the host is given but also the identification on the host of the desired page, the protocol to be used to transfer that page, and the identification of the application level entity on the host capable of handling that protocol.

## Slide 34: Inside the Web
HTTP Client
(Web Browser)
HTTP Server
HTTP Server
HTTP Server
Other Server
HTTP Server
HTTP Link
transporting HTML-
encoded hypertext
Other Data Link
Notes: The web application is clearly an example of a “many to one” information flow as data from many different websites can be merged in the client’s browser.

## Slide 35: Technically, what is the Web ?
HTTP : HyperText Transfer Protocol.
  HTTP Client : a Web Browser
    Presenting information encoded in HTML.
    Translating user interactions into the HTTP.
  HTTP Server : a process interpreting client requests
    Sending pieces of hypertext stored in HTML
    Translating information available in other formats
    acquiring information from outside the Web.
  Stateless (connectionless) communication protocol
  Uses a connection oriented transport protocol.
The WEB = Internet + HTML + URL + HTTP
Notes: The “HyperText Transfer Protocol” is the most common application level protocol used on the web.
Keeping connections at the application level with all visitors of a web site would be a heavy and useless task for a web server, especially as it would imply closing connections from all occasional visitors who forget to close their connections. For that reason, the http protocol is a connectionless protocol.
A connection oriented, encrypted alternative protocol called HTTPS is often used for applications requiring a connection and/or a high level of security.

## Slide 36: HTTP Hypertext Transfer Protocol
Network Service
Transport
entity
Transport
entity
Connection oriented protocol
Client
HTTP
Server
HTTP
Connectionless protocol
Browser
Web Server
Notes: It is important to bear in mind that connection oriented or connectionless are properties of a specific protocol, applicable to a single layer in a layered system. It is perfectly possible to use connectionless protocol at layer n while layer n-1 is connection oriented or vice-versa. Almost all combinations can be meaningful and useful in specific telecommunications environments.
It was already mentioned that http is a connectionless application layer protocol. However, when a site is visited, a page needs to be transmitted from server to client and this transmission should be errorless, which almost implies, as will be seen later, a connection oriented protocol.
Therefore, http uses TCP, a connection oriented transport protocol. Whenever a page is requested from a web server, a TCP connection is opened and closed when the entire page (possibly together with multimedia attachments) has been transmitted.

## Slide 37: HTTP is a Stateless Protocol
Benefit : performance of server
Penalty : Server can not keep information about user.
Client
HTTP
Server
HTTP
Connectionless protocol
Browser
Web Server
> show me my bank transactions
Give your name and password <
> XYZ, ******
OK, what do you want <
> show me my bank transactions
Give your name and password <
....
Notes: As http is connectionless, it is by definition, also stateless, or in other words, the application entities have no memory.
This would be clearly unacceptable for applications such as home banking, where the server would require the user to authenticate him/her-self and remember that authentication for the entire banking session.
Normally this problem is solved by using an other application level protocol, https, which is connection oriented, but for less critical applications, some tricks can do with http.

## Slide 38: HTTP is a Stateless Protocol
Logging in a stateless server :
Client
HTTP
Browser
Server
HTTP
Web Server
> I want to log into the server
Give your name and password <
> XYZ, ******
OK, here is your key 478 <
> show me my bank records,
my key is 478.
Here are your bank records <
$$$$$$$$$ <
If you need more use key 953 <
....
Notes: The trick to simulate state variables in a stateless protocol consists in sending back and forth a specific, normally invisible, message, called “Cookie” that contains the state variables that can not be stored in the application entities because of the connectionless protocol.
For instance, in a banking operation, the server could, after a successful authentication, send back a cryptographic key the user can send back with a request to see the state of his/her bank accounts. For obvious security reasons such a key should be single use and hard to guess.

## Slide 39: Web security (1)
Most attacks start with an executable program being installed remotely in a computer.
Initially, web browsers provided a “sand bag” to run remote programs, prohibiting them to access local resources such as disks.
Making web browsers the run-time environment for a multitude of application programs (“apps”) made “sandbags” too restrictive!
Only trusted apps should be allowed !!!

## Slide 40: Web security (2)
Cookies are too insecure for sensitive interactive transactions such as web banking
Use a connection oriented web protocol (HTTPS) for all personalized transactions
Encrypt the PDUs